PRESS RELEASE (No. 371)

15th september 2010	for immediate release

New ultra miniature watch crystal at Electronica 2010

IQD’s latest watch crystal design is one of the smallest in the world. Launching at Electronica 2010, the 32.768kHz IQXC-25 measures just 2.00 x1.2 x 0.6mm making it ideal when PCB real estate is at a premium. The ceramic package is a 2-pad device with an operating temperature range of -40 to +85°C and for which solder pad and layout recommendations can be provided. The crystal has a standard temperature coefficient of −0.03 +/-0.01ppm/degrees C2.

While frequently taken for granted, the humble watch crystal is fundamental to the function of millions of diverse products, from space satellites to washing machines. Its position as the lowest cost quartz crystal belies its importance in the modern world.

It is eminently suitable for all portable applications where accurate time keeping and non-volatile data storage is required via a Real Time Clock e.g. R.F.I.D, Metering, Security & Access Control, POS Terminals.

Available with an initial adjustment tolerance of +/-20ppm and a standard load capacitance of 12.5pF the IQXC-25 is also available for those applications that require a 9.0pF load. The product comes on Tape and Reel although for prototyping it is also available in bulk packaging.

Further details will be available at IQD’s stand 215 in Hall B5 at Electronica 2010.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe with active customers in over 60 countries. We offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs and Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com

Further information: 
Harriet Charles
IQD Frequency Products
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com