PRESS INFORMATION

11th November 2008	For Immediate Release

LVDS oscillator sets the pace for high-data-throughput 
computer networking applications

Electronica, Munich, 11-14 November 2008: Hall B6, Stand 264 – IQD Frequency Products announces the CFPS-60, a new SPXO (simple packaged crystal oscillator) with LVDS output for use in computer networking equipment and peripherals such as switches, hubs, routers and network interface cards.

The high-speed, low-power-dissipation characteristics of LVDS (low-voltage differential signalling) suit the CPFS-60 well to applications with very high data throughput. Data integrity is supported by fast signal rise and fall times of just 0.7ns (20% to 80%), compared to typically 5 or 6ns for a low-cost HCMOS SPXO. Phase jitter is suitably low at a maximum of 1ps RMS (12kHz to 20MHz).

The CFPS-60 offers a range of output frequencies from 75.0MHz to 170.0MHz — high for a low-cost device — and frequency stabilities of 25, 50 or 100ppm over operating temperature ranges of –40( to +85(C (industrial) or –10( to +70(C (general purpose). Shock and vibration qualification to Mil-Std-202F allows for use in both industrial environments and portable equipment.

The CFPS-60 comes as a 7 x 5mm SMD and can be supplied in tape-and reel format for automatic placement. It operates from a 3.3V supply and has tristate functionality as standard.

– Ends –

Notes for Editors:

Since its inception in 1973, IQD Frequency Products has established a leading position across Europe as a specialist manufacturer and supplier of quartz-based frequency control components. IQD offers one of the most comprehensive frequency product ranges available, from low-cost commercial-grade devices to those used in high-reliability military and professional applications. Its components, which are specified by leading manufacturers in the aerospace, communications, computing, consumer and medical industries throughout the world, include quartz crystals, crystal oscillators, MEMS oscillators, programmable oscillators, VCXOs, TCXOs, OCXOs and rubidium frequency standards. IQD has external representatives and distributors in nearly 50 countries.

Further information and enquiries:

Harriet Charles
IQD Frequency Products
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com

www.iqdfrequencyproducts.com

Issued by:

Andrew Taylor
AJT Communications
T: +44 (0)7966 398118
E: ajt-comms@zen.co.uk

IQD/007/D1