PRESS RELEASE (No. 387)

13th june 2011	for immediate release

IQD’s new design SMD OCXO delivers
high stability combined with low phase noise

IQD have unveiled their new IQOV-90 series high stability low phase noise OCXO. Designed and manufactured in Germany at their IQD FOQ GmbH facility, the new OCXO offers a range of outputs and supply voltages across a frequency range of 10 to 40MHz.

Improvements in the oscillator circuit design have reduced the typical phase noise to 
-98dBc/Hz@1Hz and -152dBc/Hz@1kHz with a noise floor of less than -157dBc/Hz. Using a high performance SC-Cut crystal, ageing behaviour of less than ±50ppb per year and short term stability of <5x10-11@1s can be achieved based on a 10MHz, 12V, sinewave output device.

With an optimised control and heating circuit design, the IQOV-90 delivers a temperature stability of better than ±5ppb over the -20 to 70 degrees C operating temperature range.

Housed in a 25.4 x 22.0mm package with a height of only 12.3mm, the new design satisfies applications where space and height is limited. Based on a FR4-PCB with a metal lid and delivered in package quantities of 75pcs per reel the IQOV-90 is suitable for fully automatic SMD production.

As standard these parts are available with supply voltages of 12V, 5.0V or 3.3V and sinewave or HCMOS output compatibility making them suitable for a wide range of applications including base stations, repeater stations, instrumentation, medical and measurement equipment. Due to the flexible nature of the design, alternative supply voltages and output compatibilities to suit almost any application can also be readily developed to meet individual customer requirements.

The IQOV-90 series can also be specified with a frequency adjustment option and additionally, a reference voltage output where required. As a further option, an oven alarm output is available which indicates when the OCXO is at a stable working condition after warm up.

Further information and full application support is available from IQD’s sales offices or via our multilingual website at www.iqdfrequencyproducts.com.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs and Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com

Further information: 
Harriet Charles
IQD Frequency Products
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com