PRESS RELEASE (No. 397)

28th FEBRUARY 2012	for immediate release

IQD launch new tight stability ‘Real Time Clock’
at Embedded World 2012

IQD have launched a newly designed tight stability Real Time Clock (RTC) which incorporates a 32.768kHz crystal with a Digital Temperature Compensated Crystal Oscillator (DTCXO). This Surface Mount RTC is housed in a plastic package with a FR4 base measuring just 10.0 x 7.4mm.

The new IQRC-100 series has an I2C-Bus* (400kHz) interface with a CMOS output allowing the RTC to operate with a very low power consumption which at 3V is typically 0.8µA. Incorporating the DTCXO within the RTC allows for a very tight frequency stability of ±3.4ppm over a wide operating temperature of –40 to +85 degrees C to be achieved. This tight stability equates to a maximum of 9 seconds a month deviation over the full operating temperature range. Other frequency stabilities are available including ±5ppm over –40 to +85 degrees C and ±5ppm at room temperature, 25 degrees C. For applications where a tight stability is not required a frequency stability of ±25ppm over –40 to +85 is available. The IQRC-100 series has an interface voltage range of between 1.8 to 5.5V and a wide timekeeper voltage range of between 1.6 to 5.5V.

The functions within the IQRC-100 series include a full calendar, alarm, timer and leap year adjustment.

The IQRC-100 series is ideal for a wide range of applications including: Blood Pressure Monitors, Data loggers, Industrial Control, POS Systems, Security Systems, Telemetric Systems & Utility Meters

Further details will be available at IQD’s stand 152 in hall 1 at Embedded Show 2012.

‘*The I2C-Bus is a trademark of NXP Semiconductors’

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com

Contacts for regional media:

| Maria Shoteh Station Road Crewkerne Somerset TA18 8AR United Kingdom T: +44 (0) 1460 270200 maria.shoteh@iqdfrequencyproducts.com | Anke Allen Raiffeisenstr. 53 74906 Bad Rappenau Germany T: +49 (0) 7264 9145-0 anke.allen@iqdfrequencyproducts.com | Sarah Bradley 7 Avenue Didier Daurat 31702 Blagnac Cedex France T: +33 (0)5 34 50 91 18 sarah.bradley@iqdfrequencyproducts.com |
| --- | --- | --- |