ELECTRONICA 2012 PREVIEW PRESS RELEASE (No. 405)

14th September 2012	for immediate release

IQD introduces ground-breaking new quartz crystal range that delivers significant space and cost saving

IQD has launched two new quartz crystal models housed in unique innovative packages that deliver significant space and cost saving whilst still utilising tried and tested technology. The new surface mount 
IQXC-74 measures just 7 x 4mm with a height of 2.3mm – this compares with the similar current industry standard HC49/4HSMX design which measures 11.4 x 4.9 x 4.3mm. Whilst IQD’s latest ceramic package designs do offer smaller dimensions than this, they are significantly more expensive due to the artificially high cost of the ceramic packaging. The IQXC-74 offers an attractive compromise at significantly lower cost.

IQD is also launching a thru-hole version, the IQXC-75 which is even smaller at 6 x 4 x 1.8mm with similar benefits. Both models are designed to provide a low-cost, high reliability timing solution in a wide range of electronics applications.

Frequencies are available from 12 to 40MHz over operating temperature ranges as wide as -40 to +85°C. Frequency tolerances and stabilities over the operating temperature range are available down to 10ppm. Drive level ranges from just 10µW to 100µW and shunt capacitance is rated at 5pF max. Frequency range changes due to aging are specified at ±5ppm in the first year.

Both models are housed in hermetically sealed metal can packages and can be supplied in tape and reel form to support use in automated assembly manufacturing processes.

Further details will be available at the IQD stand 314 in Hall B5 at Electronica 2012.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com