PRESS RELEASE (No. 410)

14th December 2012	for EMBEDDED WORLD 2013 PREVIEWS

IQD launches new ultra high stability OCXO
at Embedded World 2013

IQD’s new IQOV-70 series OCXO which is launching at Embedded World 2013 is designed for use in next generation multimode base station platforms. Operating at a frequency of 10MHz, the new model achieves a frequency stability of ±3ppb (parts per billion) over the operating temperature range of -10 to +70 degrees C.

Multimode base station platforms are based upon TD-LTE technology (Time Division Long Term Evolution) and can fully support HSDPA/MBMS/HSUPA/HSPA+ which share the same platform as LTE with its super-high capacity. This enables it to accommodate many situations including densely populated and suburban areas, rural areas and indoor locations etc.

The new design is built around an SC-cut (Stress Compensated) crystal, designed and manufactured in-house at IQD FOQ GmbH where the latest techniques in thermal modelling have been developed over many years and significantly contributes to the excellent performance.

Output capability can be either HCMOS or LV-TTL with supply voltage options of 5 or 12 Volts. Electrical frequency adjustment of ±0.4ppm min allows for ageing over time. Phase noise performance of < -155dBc/Hz at an offset of 10kHz is particularly important bearing in mind the application and its need for high capacity data transfer. Frequency ageing is limited to ±0.05ppm maximum over a period of 1 year.

As standard, the design is housed in an industry standard IEC C008 5-pin Euro package with a height of only 13mm max but surface mount packages are also available.

Further details will be available at IQD’s stand 152 in Hall 1 at Embedded World 2013.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com