PRESS RELEASE (No. 415)

26th February 2013	for immediate release

IQD launches new 14-pin DIL OCXO
at Embedded World 2013

IQD’s new IQOV-160 series OCXO which is being launched at Embedded World 2013 offers all the performance benefits of an OCXO in the small size of an industry standard 14-pin DIL package.

The new model is available in a wide frequency range from 5 to 100MHz, the most common frequencies being 10MHz, 20MHz, 12.8MHz, 13MHz, 15MHz, 16.32MHz, 16.384MHz, 18.432MHz, 19.20MHz, 19.44MHz, 20MHz, 25MHz, 26MHz, 30.72MHz, 32.768MHz, 38.88MHz, 40MHz, 50MHz and 100MHz.

The IQOV-160 series delivers a frequency stability of ±5ppb over the operating temperature range of –40 to +85 degrees C and with first year ageing limited to 0.1ppm. Storage temperature range is –55 to +105 degrees C.

Output options include Sine Wave or HCMOS with a supply voltage of 3.3V. Warm up power consumption is 2W with a warm-up time of 1 minute whilst stable power consumption is 0.6W.

Typical phase noise performance for a 10MHz version is: –85dBc/Hz at 10Hz; –130dBc/Hz at 100Hz; –150dBc/Hz at 1kHz; –155dBc/Hz at 10KHz; –160dBc/Hz at 100KHz and –160dBc/Hz at 1MHz. Harmonic is
<= -40dBc.

Applications include instrumentation, microwave radios, cellular paging base stations, broadcast equipment and home meter readers.

Further details will be available at IQD’s stand 152 in Hall 1 at Embedded World 2013.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Follow us on:   facebook  -   Twitter  -   LinkedIn  Google Plus