PRESS RELEASE (No. 413)

8th JULY 2013	for IMMEDIATE RELEASE

New IQD military oscillator withstands 100,000g shock

IQD’s new HGXO series of surface mount oscillators is designed primarily for military applications such as smart munitions and projectile electronics although the devices can also be used in demanding industrial applications. Designed around a hermetically sealed high-shock crystal and a CMOS compatible integrated circuit, the new device is able to survive shock levels of up to 100,000G and vibration levels of 20g at 10-2000Hz swept sine in accordance with MIL-STD-202G.

Housed in an industry standard 7 x 5mm 4-pad ceramic package with metal lid, 5 supply voltage versions are available at 5.0V, 3.3V, 3.0V, 2.5V and 1.8V, thus providing compatibility with the latest generation of low power chipsets. Output frequencies can be specified between 460kHz and 50MHz with a 15pF HCMOS drive capability. Frequency tolerance is available down to ±10ppm whilst frequency stability can be specified at ±40ppm over the full military temperature range of -55 to 125°C down to ±10ppm over commercial temperature ranges coupled with low frequency ageing characteristics.

Variants are also available which incorporate enable/disable and tri-state control. In keeping with its military capability the range can be specified with a number of termination finishes including tin/lead where to use a device that is RoHs compliant would cause approval issues. However RoHs compliant finishes are also available for less sensitive applications. Duty cycle is 40% min and 60% max with a start-up time of 5ms max and a rise and fall time of 6ns max. Packaging options include tray pack or tape and reel.

The HGXO range is part of a comprehensive range of military specified products available from IQD covering both high specification crystals as well as oscillators. Full details are available from any of IQD’s sales offices.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist high performance product manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Crystal Filters, Real Time Clock, SAW Filters and VCOs & Synthesisers.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:    facebook  -   Twitter  -   LinkedIn  Google Plus