PRESS RELEASE (No. 421)

20th August 2013	for IMMEDIATE RELEASE

IQD introduces ultra-miniature crystal only 0.5mm high

IQD Frequency Products has launched one of the world’s smallest quartz crystals, the IQXC-42 which measures just 2.0 x 1.6mm with a height of only 0.5mm. The new ultra-miniature model is especially suitable for many portable applications such as hand held inventory control devices, battery powered telemetry equipment, notebook computers and surveillance devices.

The IQXC-42 crystal is available in frequencies between 20MHz and 50MHz and operates over the full industrial temperature range of -40 to +85C. Frequency stabilities can be specified as low as ±10ppm over the commercial temperature ranges. In line with the requirements of the latest generation of microprocessors the load capacitance can be as low as 8pF.

Housed in a 4-pad ceramic package with a hermetically sealed metal lid which helps to minimise the EMI radiation, the product is designed to able to withstand shock levels of up to 1000G in accordance with IEC 60068-2-27. The IQXC-42 is available on tape and reel for automatic assembly as well as loose in bulk pack for low volume prototypes.

Further details are available from all of IQD’s sales offices.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist high performance product manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Rubidium Oscillators, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Crystal Filters, Real Time Clock, SAW Filters and VCOs.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:    facebook  -   Twitter  -   LinkedIn  Google Plus