PRESS RELEASE (No. 437)

12th SEPTEMBER 2014	for immediate release

IQD’s new specialist high shock oscillator also delivers high temperature performance

The new SQXO-2ATHG range of very high shock survivability oscillators launched by IQD are housed in a 
TO-39 package and can withstand shock levels of up to 8,000g for 0.5ms, ½ sine. They are designed primarily for applications such as underground boring tools, down hole instrumentation and avionics applications including flight recorder equipment and on board computers.

Frequencies are available from 32.768kHz up to 50MHz and can be specified to operate from either a 3.3V or 5V supply providing an CMOS output and a start up time of under 5ms. High temperature is catered for with variants being available which operate up to 200 degrees C.

Current consumption is down to 3.0mA which again lends itself to applications in remote locations where easy access is not always possible. Standard packaging is in a tray and the devices are fully RoHS compliant.

Further information is available from all IQD's worldwide sales offices with full applications support.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Rubidium Oscillators, Automotive Crystals to AEC-Q200 & TS16949 release and Real Time Clock,.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:    facebook  -   Twitter  -   LinkedIn  Google Plus