PRESS RELEASE (No. 444)

19th may 2015	for immediate release

New miniature Low Power TCXO/VCTCXO
launched by IQD at IMS 2015

Housed in a small 2.0 x 2.5 x 0.8mm ceramic package, IQD’s new IQXT-260 series of digitally compensated  TCXOs,  launching at IMS 2015, employs an analogue ASIC for the oscillator and a high order temperature compensation circuit that provides a smoother signal. With a maximum current consumption of only 2mA, the IQXT-260 offers stabilities down to ±0.5ppm over an operating temperature range of -40 to 85°C with a clipped sinewave output. Operating from 1.8 to 3.3V, the new range is available in three versions: TCXO, VCTCXO & TCXO with enable/disable function, all across a frequency range of 10 to 52MHz. The version with the enable/disable option only requires a standby current of typically <0.01µA, which is ideal for battery operated equipment.

As frequency bands such as 2.4GHz become overcrowded and the bandwidths need to be narrower, the precise signal and tighter frequency stability of a TCXO solution is ideal plus frequency slope and perturbation specifications can be customised to suite application requirements. The IQXT-260's high stability, low power consumption, small footprint and powerful compensation method makes this new TCXO ideally suited for demanding GPS mobile applications including Portable Navigation Devices as well as Wi-Fi, WiMax, WLAN and Ethernet applications.

Full details will be available at IQD’s booth 2915 at IMS 2015.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Advanced OCXO modules, Rubidium Oscillators and Automotive Crystals to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com