PRESS RELEASE (No. 446)

25th August 2015	FOR IMMEDIATE RELEASE

New miniature OCXO from IQD measures only 9.7 x 7.5mm

IQD’s latest Oven Controlled Crystal Oscillator (OCXO), the IQOV-71 series, is housed in 4-pad plastic package with a fibre glass base measuring only 9.7 x 7.5mm. Despite the ultra-small size, the new model offers very low frequency stabilities down to ±10ppb over an operating temperature range of -20 to 70 degrees C or ±20ppb over -40 to 85 degrees C making it a class leader for this type of high performance device.

Standard frequencies available are 10MHz, 12.8MHz, 19.2MHz, 20MHz, 24.576MHz, 25MHz, 30.72MHz, 38.88MHz, 40MHz, 49.152MHz and 50MHz which will satisfy most typical applications. Other frequencies in the range 5MHz to 50MHz can be developed for commercially viable quantities. Critically, power consumption is typically less than 1 Watt during warm up which only takes approximately 3 minutes and less than 0.4Watts once the device has reached steady state. Frequency ageing is less than 2ppb per day and a maximum of 3ppm over a 10 year period.

The IQOV-71 offers either a standard HCMOS or Clipped sinewave output, with operating voltages specified at either 3.3V or 5.0V. Low phase noise performance is assured with figures of -152dBC/Hz at 10kHz offset and only -153dBc/Hz at 100kHz from the carrier. Unusually for this type of device, the G-sensitivity is also good at <2ppb/G making the design suitable for applications such as military radios and airborne applications.

In order to maximise flexibility there is an option to specify external frequency adjustment by the application of a variable control voltage that allows for crystal ageing as well as changes in the circuit conditions. This variation is also extremely linear being <1% as against a more typical 5%.

This part is intended for a wide range of applications including Picocells for the ever increasing rage of wireless applications, satellite communication, broadcasting, microwave and instrumentation such as frequency counters and analysers.

###

Notes for Editors:

Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Advanced OCXO modules, Rubidium Oscillators and Automotive Crystals to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information:

Harriet Burrow
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.burrow@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com