PRESS RELEASE (No. 448)

21st October 2015	FOR IMMEDIATE RELEASE

IQD introduces new range of Automotive 
Clock Oscillators to AEC-Q200 & TS16949

IQD has launched a new range of clock oscillators designed for applications that require AEC-Q200 & TS16949 automotive grade products. The new models, housed in a ceramic seam sealed packages, are available in five different industry standard sizes, 2 x 1.6, 2.5 x 2, 3.2 x 2.5, 5 x 3.2 and 7 x 5mm. All are available with full PPAP documentation from levels 1 to 5 and are suited for extreme environments found in typical automotive applications including ABS and Airbag sensors, Engine Control Units (ECU), High speed automotive networks and Tyre Pressure Monitoring System (TPMS) receivers.

All of the new models operate over the standard automotive operating temperature range of -40 to 125 degrees C. Frequency stability options can be specified down to ±50ppm or ±25ppm over the industrial operating temperature range of -40 to +85 degrees C, which covers all applications be it in the engine compartment or in cab. With the increasing need to reduce power, even inside vehicles, the clock oscillators are available in three different voltages, 1.8, 2.5 and 3.3V. Typical current consumption on the 1.8V versions of the IQXO-542 AUTO and CFPS-53 AUTO models is only 3mA.

All models deliver a CMOS output, 15pF load with a rise and fall time of typically 5 to 7ns and the option of a Tri-State function on Pin 1.  Low frequencies, such as 1MHz in the 7 x 5mm or 4MHz in the 2 x 1.6mm oscillators which are not possible in the same sized packaged quartz crystal, are also available. The highest frequency available is 135MHz in the CFPS-73 AUTO & IQXO-581 AUTO models with the others being typically 50MHz.

The new range of automotive grade clock oscillators compliments IQD‘s existing range of automotive grade quartz crystals. For further information please visit www.iqdfrequencyproducts.com or contact one of our sales offices.

###

Notes for Editors:

Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Advanced OCXO modules, Rubidium Oscillators and Automotive Crystals to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information:

Harriet Burrow
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.burrow@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com