PRESS RELEASE (No. 451)

?? APRIL 2016	FOR IMMEDIATE RELEASE

IQD launch world’s smallest 32.768kHz clock oscillator

IQD have launched what they believe to be the world’s smallest 32.768kHz clock oscillator in a design that also delivers very low power. Measuring just 1.6 x 1.2 x 0.7mm, the new model is housed in a hermetically sealed ceramic package. With a current consumption of only 30µA and with a standby current as low as 3µA, this ultra-low power clock oscillator is ideal for use in hand held and battery powered applications and where accuracy is required in real time clocks. Typical applications include battery management systems, communication modules and systems (Bluetooth, Wi-Fi, Wireless LAN & Zigbee), LCD lighting systems and smart meters (AMR).

The new range delivers better temperature characteristic than standard 32.768kHz tuning fork crystal based oscillators due to the use of an AT-cut crystal normally found in higher frequency oscillators. Start-up time is only 7ms at 3.3V with a rise and fall time of 200ns.

These CMOS based oscillators are available in three supply voltages: 1.8V (IQXO-986), 2.5V (IQXO-985) and 3.3V (IQXO-984) with frequency stabilities of ±30ppm over an operating temperature range of -20 to 70 degrees C or ±50ppm over -40 to 85 degrees C.

Full specifications and data sheets are available at www.iqdfrequencyproducts.com

###

Notes for Editors:

Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Clock Oscillators, VCXOs, TCXOs, OCXOs, GPS Disciplined OCXOs, Rubidium Oscillators, Automotive Crystals to AEC-Q200 & TS16949 release and Automotive Oscillators to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information:

Harriet Burrow
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.burrow@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:   facebook  -   Twitter  -   LinkedIn  Google Plus