PRESS RELEASE (No. 459)

10th NOVEMBER 2016	ELECTRONICA NEWS FOR IMMEDIATE RELEASE

New range of ultra miniature low phase noise
VCXOs launched by IQD at Electronica 2016

IQD’s new IQXV-93 series Voltage Controlled Crystal Oscillator (VCXO) delivers ultra low phase noise of 131dBc/Hz at 100kHz and RMS phase jitter as low as 0.9ps (12kHz to 20MHz) in a 2.5 x 2.0 x 1.0mm industry standard 6-pad ceramic hermetically sealed package.

Available over a very wide frequency range from 8MHz to 1.5GHz, the new model is ideal for applications such as 10G & 40G Ethernet, Fibre networking, SDH/SONET, WiMax and WLAN. Two supply voltages are available, 2.5 and 3.3V, with a stability down to ±10ppm over an operating temperature range of -40 to +85 degrees C.

The frequency can be adjusted externally by the application of a control voltage (1.65V nominal) which can pull the output frequency by a minimum APR of ±35ppm. This allows for absolute frequency adjustment and a correction for crystal ageing. There is also an enable/disable option on pin 2 which allows the VCXO to be switched off by using simple logic control. Full data sheets are available on IQD’s website at www.iqdfrequencyproducts.com

###

Notes for Editors:

Backed by over 40 years’ experience in the manufacture of frequency products, IQD is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability industrial, automotive and military grade applications including: Quartz Crystals, Clock Oscillators, AEC-Q200/TS16949 Crystals & Oscillators, VCXOs, TCXOs, OCXOs, GPS Disciplined OCXOs, and Rubidium Oscillators.

Manufacturing capacity totals over 40 million units per month covering quantities from one off specials to multi-million unit orders. In addition, IQD offers customers a range of engineering support services including: application support, custom product design, sample development, electrical testing & screening, frequency/temperature testing, accelerated ageing, circuit characterisation and MTIE/TDEV testing. IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. For more information, visit www.iqdfrequencyproducts.com.

Further information:

Harriet Burrow
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.burrow@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:   facebook  -   Twitter  -   LinkedIn  Google Plus