PRESS RELEASE (No. 462)

February 2017	FOR IMMEDIATE RELEASE

Ultra-Miniature Watch Crystal for IoT Applications

Measuring just 2.0 x 1.2mm and with a height of only 0.6mm, IQD's 32.768kHz IQXC-25 watch crystal is ideal for applications where space on a PCB is at a premium. It is housed in a 2-pad ceramic package with an operating temperature range of -40 to +85 degrees C and a standard frequency stability coefficient of -0.03 ±0.01ppm/degrees C². Standard frequency tolerance is ±20ppm however ±10ppm can also be manufactured upon request whilst the load capacitance can be specified at 12.5pF, 9pF, 7pF or 6pF.

The IQXC-25 is ideal for the many applications related to the Internet of Things (IoT) where accurate time keeping and non-volatile data storage is required via a Real Time Clock (RTC). These include battery management, Bluetooth, POS terminals, smart meters, wearables and Wi-Fi.

The standard part numbers are: LFXTAL050789 (12.5pF), LFXTAL051643 (9pF), LFXTAL059461 (7pF) and LFXTAL065455 (6pF) and these are available on Tape and Reel (REEL) or on Cut Tape (CUTT).  All variants are available either direct from IQD or via our extensive range of worldwide distributors with live stock visibility available on our website at www.iqdfrequencyproducts.com.

###

Notes for Editors:

Backed by over 40 years’ experience in the manufacture of frequency products, IQD is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability industrial, automotive and military grade applications including: Quartz Crystals, Clock Oscillators, AEC-Q200/TS16949 Crystals & Oscillators, VCXOs, TCXOs, OCXOs, GPS Disciplined OCXOs, and Rubidium Oscillators.

Manufacturing capacity totals over 40 million units per month covering quantities from one off specials to multi-million unit orders. In addition, IQD offers customers a range of engineering support services including: application support, custom product design, sample development, electrical testing & screening, frequency/temperature testing, accelerated ageing, circuit characterisation and MTIE/TDEV testing. IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. For more information, visit www.iqdfrequencyproducts.com.

Further information:

Carly Gray
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: Carly-Rose.Gray@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:   facebook  -   Twitter  -   LinkedIn  Google Plus