PRESS RELEASE (No. 394)

3rd FEBRUARY 2012	for immediate release

IQD launches new range of ultra-miniature TCXOs

IQD have launched a new range of ultra-miniature SMD TCXOs, the IQXT-170 series. Housed in a tiny 2.0 x 1.6 x 0.8mm ceramic package, they are available with a clipped sinewave output with or without a voltage control option.

The new TCXOs are offered with two supply voltages, 2.8V and 3.0V and standard frequencies of 13.0, 19.2, 26.0, 38.4 and 52.0MHz. A frequency stability of ±1ppm is available over a an operating temperature range of
-10 to +75 degrees C and ±2ppm over a wider operating temperature range of -30 to +85 degrees C. The voltage control option is available with a pulling range of ±8ppm to ±15ppm.

The very small package size makes this series ideally suited for wireless telecommunication applications where board space is limited. Examples are 3G-applications, such as CDMA, W-CDMA, TD-SCDMA, as well as GPRS, GSM, Wi-Fi, WiMAX.

Further details will be available at the IQD stand 152 in Hall 1 at Embedded World 2012.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs and Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com