PRESS RELEASE (No. 395)

28th FEBRUARY 2012	for immediate release

IQD launches new range of ultra-miniature SAW Filters

IQD has launched a new range of ultra-miniature surface mount RF Surface Acoustic Wave (SAW) filters. Measuring just 3.0 x 3.0 x 1.4mm, these miniaturised SAW Filters are housed in a hermetically sealed ceramic package.

The IQSF-103 series has a centre frequency of between 300MHz and 2.8GHz and a bandwidth of 0.1 to 85MHz. The product is available with a low insertion loss of <3dB and a high attenuation of typically -55dB and can operate over a temperature range of –40 to +85 degrees C. Custom specifications are available on request.

This filter, which is certified to TS16949 & AEC-Q200, is ideal for a wide range of applications including: T.P.M.S, Remote Keyless Entry, AMR/AMI Metering, RFID, Wi-Fi, WiMAX, Basestations, LTE, STB and Cable Modems.

Further details will be available at IQD’s stand 152 in hall 1 at Embedded Show 2012.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com

Contacts for regional media:

| Maria Shoteh Station Road Crewkerne Somerset TA18 8AR United Kingdom T: +44 (0) 1460 270200 maria.shoteh@iqdfrequencyproducts.com | Anke Allen Raiffeisenstr. 53 74906 Bad Rappenau Germany T: +49 (0) 7264 9145-0 anke.allen@iqdfrequencyproducts.com | Sarah Bradley 7 Avenue Didier Daurat 31702 Blagnac Cedex France T: +33 (0)5 34 50 91 18 sarah.bradley@iqdfrequencyproducts.com |
| --- | --- | --- |