PRESS RELEASE (No.408)

10th OCTOBER 2012	for immediate release

IQD launches new series of fast make programmable oscillators with class leading phase jitter performance

The short lead-times offered by programmable oscillators are typically offset by relatively poor performance in comparison to standard crystal oscillators, especially as regards phase noise and jitter. IQD’s two new ranges of programmable oscillators offer the best of both worlds with phase jitter performance comparable to traditional crystal oscillators combined with lead-times as short as 3 days.

Both models, the IQXP-20 clock oscillator and the IQXP-30 voltage controlled oscillator, offer RMS phase jitter down to 0.4ps across all output types. A very wide frequency range from 10.0MHz up to 1.5GHz is available from along with HCMOS output capable of driving 15pF; LVPECL & LVDS outputs are also available at the higher frequencies.

Frequency stabilities down to ±10ppm and operating temperature ranges out to -40 to +85 degrees C are available along with the option to specify all inclusive stabilities including temperature range, supply variations, load variations and 15 years ageing at 25°C. Customers can choose from 2.5V or 3.3V supply for both models, both of which are housed in a 5.0 x 3.2mm hermetically sealed ceramic package only 1.2mm high

The IQXP-30 VCXOs are available with a total pull range of ±50ppm minimum and a control voltage nominal of 1.65V.

With such a wide frequency range, low phase jitter performance, short lead-times and competitive prices, both models are ideal for use by design engineers on new projects where design-in samples are required on short lead-times as well as for use in mass production in a wide range of applications including Gigabit Ethernet, Video, Telecoms, SCSI, SAS & SATA.

###

Notes for Editors:
Backed by a pedigree that has been developed over nearly 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist OCXO manufacturing division, IQD FOQ GmbH in Germany. With active customers in over 60 countries, IQD offer one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications. Our range includes Quartz Crystals, Crystal Oscillators, Silicon/MEMS Oscillators,  Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals & Oscillators to AEC-Q200 & TS16949 release, Real Time Clock and SAW Filters.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com