PRESS RELEASE (No. 428)

27TH january 2014	EMBEDDED WORLD 2014 PREVIEW

New analogue compensated TCXO from IQD delivers a frequency stability down to ±0.28ppm

Portable instrumentation equipment and communications systems (fixed and mobile) frequently require a high stability oscillator but don’t have either the physical space for or power to drive an Oven Controlled Crystal Oscillator (OCXO). IQD's latest TCXO launching at Embedded World 2014 provides a practical alternative and is designed specifically for such applications.

Housed in an industry standard 7 x 5mm ceramic package, the new IQXT-200 series offers a class leading frequency stability down to ±0.28ppm across a wide frequency range from 10MHz up to 50MHz. Operating over the standard industrial temperature range from -40 to 85 degrees C, users can select variants to operate off a 3.0V, 3.3V or 5.0V power supply with the current drawn being typically less than 5mA. A wide range of outputs can be specified including HCMOS or Clipped Sine Wave.

Versions are also available which allow the use of an external voltage to control the pullability which caters for applications where the output frequency needs to be locked. All devices are RoHS compliant, reflow soldering compatible and supplied on tape & reel.

Further details will be available at IQD’s stand 650 in Hall 4 at Embedded World 2014.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. We have operations in America, Asia and Europe including our specialist high performance product manufacturing division, IQD FOQ GmbH in Germany where we offer a full custom design service, with special emphasis on low phase noise OCXOs based around our own in-house manufactured SC-cut crystals. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Automotive Crystals to AEC-Q200 & TS16949 release, Real Time Clock, and SAW Filters.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers. Our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct from all of our offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:    facebook  -   Twitter  -   LinkedIn  Google Plus