PRESS RELEASE (No. 439)

27th october 2014	ELECTRONICA PREVIEW

Electronica launch for IQD’s new GPS disciplined OCXO

IQD’s newest addition to its range of advanced oscillator modules is its IQCM-110 series of GPS disciplined OCXOs. Being unveiled at Electronica 2014, the new design incorporates an internal GPS receiver with a 1PPS output and is housed in a 14-pin 60mm square package. When coupled to an external aerial via the incorporated SMA connector, in the event of the loss of the GPS signal the highly specified 10MHz OCXO will switch-in with a holdover capability of 1.5 µSeconds for a 24-hour period thereby maintaining lock until restoration of the reference signal.

The standard operating temperature range of the module is -20 to 75 degrees C but other temperature ranges and holdover specifications can be considered upon request. The required power supply is 5V with the output being standard HCMOS. Current consumption is 2A maximum during warm-up with this reducing to 1A once the steady-state condition is reached.

The design incorporates an internal adaptive algorithm which enables the module to ‘learn’ the parameters of the GPS signal after a period of 2 days of lock so that the holdover function can start in the event of signal failure. An internal alarm is built-in to indicate lock failure and subsequent restoration of signal. In addition, the unit incorporates a serial connection for more detailed interrogation of the device’s performance.

Intended for a range of applications including land based telecommunications systems as well as marine based navigation systems the IQCM-110 forms part of a range of highly specified modules and Oven Controlled Crystal Oscillators available from IQD.

Full details will be available at IQD’s stand 314 in Hall B5 at Electronica 2014.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Advanced OCXO modules, Rubidium Oscillators and Automotive Crystals to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com