PRESS RELEASE (No. 442)

24th february 2015	for immediate release

IQD launches high holdover capability 
Precision Time Protocol (PTP) 1588 compatible Clock Module

The new IQCM-300 precision Clock Module from IQD Frequency Products is designed to provide an easy to use holdover capability for GPS receivers. Housed in a 75mm square 28-pad metal surface mount package, the IQCM-300 provides ideal protection against deliberate GPS jamming and weather outages for applications including network base stations, clock sources, clock servers and IP backhaul.

Incorporating an internal high specification HCMOS Oven Controlled Crystal Oscillator (OCXO) as backup in case of failure of the GPS signal, the module achieves a holdover specification of 1.5µs over a 24-hour period by using an adaptive algorithm. This adaptive algorithm is normally built up over a period of 2 days operation when a good and constant GPS signal is present. In the case of failure of the 1PPS input from the GPS signal then an internal alarm will indicate its failure and consequent loss of lock and transfer to free-run using the OCXO.

The module also has transmit and receive Serial Gigabyte Media Independent Interface (SGMII) ports to enable communication over the Ethernet for high speed data transfer so increasing its overall capability.

Operating from a 5V power supply which has the capability of providing a maximum current consumption of 2A during the warm up and stabilisation period but reduces to 1A once the steady state condition has been reached whilst tolerating relatively high levels of PSU ripple.

The module has a standard operating temperature range of -20 to 75 degrees C although other temperature ranges and outputs may be available on request as well as alternative holdover specifications.

###

Notes for Editors:
Backed by a pedigree that has been developed over 40 years, IQD Frequency Products is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability military and professional grade applications, including: Quartz Crystals, Crystal Oscillators, Fast Make Oscillators, VCXOs, TCXOs, OCXOs, Advanced OCXO modules, Rubidium Oscillators and Automotive Crystals to AEC-Q200 & TS16949 release.

Quality and customer service are the cornerstones of our success and we are absolutely focussed on consistently meeting and exceeding customer expectations. We take a partnership approach to working with our customers and our experienced multilingual Sales and Application Support teams guide customers from design stage through to full production.

IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. We work with several premier chip-set designers on a variety of key projects and hold approvals on a number of products including high specification oscillators. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. Full contact details are available on our website at www.iqdfrequencyproducts.com.

Further information: 
Harriet Charles
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com