PRESS RELEASE (No. 456)

19th october 2016	ELECTRONICA PREVIEW FOR IMMEDIATE RELEASE

Ultra Miniature TCXO from IQD
measure only 1.6 x 1.2mm

The latest TCXO design launched by IQD delivers two new models housed in ultra-miniature 1.6 x 1.2 x 0.45mm hermetically sealed ceramic packages that are amongst the smallest available on the market. The IQXT-350 series is a standard TCXO (Temperature Compensated Crystal Oscillator) whilst the IQXT-351 series version offers full VCTCXO (Voltage Controlled Temperature Compensated Crystal Oscillator) functionality.

Both models are initially available in four standard frequencies; 19.2, 26.0, 38.4 and 52.0MHz, all with a frequency tolerance of ±1.5ppm and frequency stability of ±0.5ppm. Both series operates at 1.8V with a maximum current consumption of only 1.7mA and a clipped sinewave output with 10kΩ//10pF drive capability.
The 26.0 & 52.0MHz parts are available with an operating temperature range of -40 to +85 degrees C whilst the 19.2 & 38.4MHz operate over -30 to +85 degrees C. Start-up time from the power mode is only 2ms max whilst the IQXT-351 (VCTCXO) series has a pullability of between ±8ppm to ±13ppm. Harmonic distortion is 
- 5.0dBc max and typical phase noise is -135dBc/Hz at 1kHz with ageing at ±1ppm max per year.

The low power and ultra-miniature footprint of both designs makes these new models ideal for GPS, IoT, Wearables, Wi-Max and Wireless Communications applications.

Full data sheets are available on IQD’s website at www.iqdfrequencyproducts.com or for further advice, speak to a member of our Applications Support Team.

###

Notes for Editors:

Backed by over 40 years’ experience in the manufacture of frequency products, IQD is a recognised market leader in the frequency control market. With active customers in over 60 countries, IQD offers one of the most comprehensive frequency product ranges available, from low cost commercial grade product to that used in high reliability industrial, automotive and military grade applications including: Quartz Crystals, Clock Oscillators, AEC-Q200/TS16949 Crystals & Oscillators, VCXOs, TCXOs, OCXOs, GPS Disciplined OCXOs, and Rubidium Oscillators.

Manufacturing capacity totals over 40 million units per month covering quantities from one off specials to multi-million unit orders. In addition, IQD offers customers a range of engineering support services including: application support, custom product design, sample development, electrical testing & screening, frequency/temperature testing, accelerated ageing, circuit characterisation and MTIE/TDEV testing. IQD’s products are specified by leading manufacturers in the aerospace, automotive, communications, computing, consumer, industrial, medical and military industries throughout the world. Our full range of products is available direct through our sales offices or via our extensive worldwide distribution and representative network. For more information, visit www.iqdfrequencyproducts.com.

Further information:

Harriet Burrow
IQD Frequency Products Ltd
T: +44 (0)1460 270200
E: harriet.burrow@iqdfrequencyproducts.com
W: www.iqdfrequencyproducts.com

Join us on:   facebook  -   Twitter  -   LinkedIn  Google Plus